## Slide 1: EEEN 311 Logic Circuits & Microprocessors
The x86 Microprocessor
[Week 11]

## Slide 2: MACROS
To make programming easier there are some common functions that can be included in your program.
Use the INCLUDE directive followed by a file name.
Compiler automatically searches for the file in the same folder where the source file is located, and if it cannot find the file there - it searches in Inc folder.

## Slide 3: MACROS
Macros are just like procedures, but not really. Macros look like procedures, but they exist only until your code is compiled, after compilation all macros are replaced with real instructions. If you declared a macro and never used it in your code, compiler will simply ignore it.
Macro definition:
name MACRO [parameters,...]
<instructions>
ENDM

## Slide 4: Example
MyMacro MACRO p1, p2, p3
MOV AX, p1
MOV BX, p2
MOV CX, p3
ENDM
ORG 100h
MyMacro 1, 2, 3
MyMacro 4, 5, DX
RET

## Slide 5: MACROS
Procedure you should use CALL instruction :
  CALL MyProc
When you want to use a macro, you can just type its name. For example:
  MyMacro
Procedure is located at some specific address in memory, and if you use the same procedure 100 times, the CPU will transfer control to this part of the memory.
Macro is expanded directly in program's code. So if you use the same macro 100 times, the compiler expands the macro 100 times, making the output executable file larger and larger, each time all instructions of a macro are inserted.
You should use stack or any general purpose registers to pass parameters to procedure.
To pass parameters to macro, you can just type them after the macro name. For example: MyMacro 1, 2, 3
To mark the end of the macro ENDM directive is enough.
To mark the end of the procedure, you should type the name of the procedure before the ENDP directive.

## Slide 6: emu8086.inc
emu8086.inc is a good example of how macros can be used
emu8086.inc defines the following macros:
PUTC char - macro with 1 parameter, prints out an ASCII char at current cursor position.
GOTOXY col, row - macro with 2 parameters, sets cursor position.
PRINT string - macro with 1 parameter, prints out a string.
PRINTN string - macro with 1 parameter, prints out a string. The same as PRINT but automatically adds "carriage return" at the end of the string.
CURSOROFF - turns off the text cursor.
CURSORON - turns on the text cursor.

## Slide 7: emu8086.inc
include emu8086.inc
ORG 100h
PRINT 'Hello World!'
GOTOXY 10, 5
PUTC 65 ; 65 - is an ASCII code for 'A'
PUTC 'B'
RET ; return to operating system.
END ; directive to stop the compiler.

## Slide 8: Procedure Remainder
ORG 100h
MOV AL, 1
MOV BL, 2
CALL m2
CALL m2
CALL m2
CALL m2
RET ; return to operating system.
m2 PROC
MUL BL ; AX = AL * BL.
RET ; return to caller.
m2 ENDP
END

## Slide 9: emu8086.inc
emu8086.inc also defines the following procedures:
PRINT_STRING - procedure to print a null terminated string at current cursor position, receives address of string in DS:SI register. To use it declare: DEFINE_PRINT_STRING before END directive.
PTHIS - procedure to print a null terminated string at current cursor position (just as PRINT_STRING), but receives address of string from Stack. The ZERO TERMINATED string should be defined just after the CALL instruction. For example:
CALL PTHIS db 'Hello World!', 0 To use it declare: DEFINE_PTHIS before END directive.
GET_STRING - procedure to get a null terminated string from a user, the received string is written to buffer at DS:DI, buffer size should be in DX. Procedure stops the input when 'Enter' is pressed. To use it declare: DEFINE_GET_STRING before END directive.
CLEAR_SCREEN - procedure to clear the screen, (done by scrolling entire screen window), and set cursor position to top of it. To use it declare: DEFINE_CLEAR_SCREEN before END directive.

## Slide 10: emu8086.inc
SCAN_NUM - procedure that gets the multi-digit SIGNED number from the keyboard, and stores the result in CX register. To use it declare: DEFINE_SCAN_NUM before END directive.
PRINT_NUM - procedure that prints a signed number in AX register. To use it declare: DEFINE_PRINT_NUM and DEFINE_PRINT_NUM_UNS before END directive.
PRINT_NUM_UNS - procedure that prints out an unsigned number in AX register. To use it declare: DEFINE_PRINT_NUM_UNS before END directive.
To use any of the above procedures you should first declare the function in the bottom of your file (but before END!!), and then use CALL instruction followed by a procedure name. For example:

## Slide 11: Example
include 'emu8086.inc'
ORG 100h
LEA SI, msg1 ; ask for the number
CALL print_string ;
CALL scan_num ; get number in CX.
MOV AX, CX ; copy the number to AX.
; print the following string:
CALL pthis
DB 13, 10, 'You have entered: ', 0
CALL print_num ; print number in AX.
RET ; return to operating system.
msg1 DB 'Enter the number: ', 0
DEFINE_SCAN_NUM
DEFINE_PRINT_STRING
DEFINE_PRINT_NUM
DEFINE_PRINT_NUM_UNS ; required for print_num.
DEFINE_PTHIS
END ; directive to stop the compiler.